## Slide 1: Configuration
Arduino
  Install rosserial library
  According the serial port, need to modify the number and baud rate of the serial port, which will be used in this project, in \Arduino\libraries\Rosserial_Arduino_Library\src\ ArduinoHardware.h and ros.h
TX2
  Install rosserial package
Reference http://wiki.ros.org/rosserial_arduino/Tutorials/Arduino%20IDE%20Setup

## Slide 2: Files
Read_gps: a testing program to read and publish a gps topic
Ros_sensor: a program to read rssi and gpa messages and publish them. Meanwhile, subscribe pwm_topic to rotate the system motor.

## Slide 3: Start Commands
Start roscore
Run the following command in a TX2 terminal:
rosrun rosserial_python serial_node.py _port:=/dev/ttyACM0 _baud:=115200
Modify the port and baud rate depending your configuration.